## Slide 1
 | Tie Down Details | Client: XXX Address: XXX XXXX
 | Project: XXXXXXX | 
Bottom Plate Hold Downs Locations - Plan
Panel Junction
Typical Connection
Tie Down Bolt Selection
Low Uplift Capacity – 4.8kN limit state
Use M6 x 75mm Ankascrew with 5mm thick round washer
High Uplift Capacity – 12.7kN limit state
Use M12 x 100mm Ankascrew with 40 x 40 x 5mm square washer into bent tab

## Slide 2
 | Wall Connection Details | Client: XXX Address: XXX XXXX
 | Project: XXXX | 
Load Bearing to Non-LB Wall Connections
Typical Connection
Connecting Non-load bearing walls to roof trusses
All wall panels to be screwed together with minimum 8 x 10-16x16 hex head or 12-14x20 hex head fasteners

## Slide 3
 | Truss Tie Down Connection Details | Client: XXX Address: XXX XXXX
 | Project: XXXXX | 
Truss & Rafter – Wall Connections
Scan this QR Code for more information on installing the ENDUROTRUSS® system
Scan this QR Code to view the installation videos
Scan this QR Code for more information on installing the ENDUROWALL® system
Scan this QR Code for more information on installing the ENDUROFLOOR™ system
All ENDUROGRIP brackets connected with 2 x M6-1Px18mm brackets on each side

## Slide 4
 | Roof Bracing Connection Details | Client: XXX Address: XXX XXXX
 | Project: XXX | 
Top Chord Bracing
Hip rafter details
Bottom Chord Bracing